## Slide 1: Electro-bio meeting
Nov. 11

## Slide 2: Categorizing performance ranges
 | Faradaic Efficiency | Current Density | Cell Voltage | Single-Pass Conversion of CO2 | Chemicals in this Tier
Tier 1a | 5 | 20 | n/r | n/r | glycolaldehyde
Tier 1b | 60 | 20 | n/r | n/r | Acetaldehyde, Ethylene Glycol,
Tier 2 | 50 | 200 | n/r | n/r | MeOH, EtOH, n-PrOH (alcohols)
Tier 3 | 70 | 300 | 4 | 20 | Ethylene, Acetic Acid*, CO, Formic Acid
Tier 4 (targets, not yet obtained) | 90 | 500 | __ | 60 | 
*Acetic acid more commonly produced from CO
** Very few reports on acetaldehyde and glycoaldehyde
*** Single-pass conversion of CO2 is often not reported; a relatively new metric to track

## Slide 3: Separation Costs
Generalize liquids with distillation
  Calculate volumetric flow rate of liquid products and electrolyte
  Use reference cost for 1000 L/min to scale distillation cost
Generalize gaseous products with pressure-swing adsorption (PSA)
  Calculate flow rate of gaseous products, side products, and unreacted CO2
  Use reference cost for 1000 m3/h to scale the PSA cost
Process | Phase | Operating Cost (kWh/m3) | Operating Cost ($/day) | Reference Capital Cost ($) | Reference Capacity (m3/h) | Reference Capacity (L/min) | Capacity Scaling Factor
PSA | GAS | 0.25 | / | 1989043 | 1000 | / | 0.7
Distillation | LIQUID | / | 17078.91 | 4687910 | / | 1000 | 0.7

## Slide 4: Reviewer Notes
R1Q2: For the eCO2R step, electricity cost is the largest fraction in most cases and therefore the voltage, current density and Faradaic efficiency are quite important in the cost analysis. If I understand correctly, the electricity costs in Figure 1c and 1d are calculated based on the parameters in Table 1, where the current density and FE are assumed to be quite high (300-500 mA/cm2 and 80-90%). It is reasonable for CO, formate and ethanol, but for other products, especially acetaldehyde, ethylene glycol and glycolaldehyde, it is very rare to achieve such high current density and FE at the same time. The authors should calculate the electricity cost for each eCO2R product in a case-by-case way, and use the parameters that are actually reported in literatures rather than assuming the same parameters for all products.
Addressed by categorizing products
Distinguish between 3 categories of present-day status and the prospective future scenario
R1Q3: Following point 2, Figure 2b can be misleading in the voltage calculation. It makes the readers think that the electricity costs in Figure 2c and 2d are calculated based on the voltage provided in Figure 2b - but actually Figure 2b only shows thermodynamic potentials. In fact I don't think the authors need Figure 2b here - a positive thermodynamic potential doesn't mean the product is easy to make. The authors can simply remove Figure 2b.
- Move 2b to SI,

## Slide 5
R1Q4: The authors did not consider the cost for product separation and justify that by pointing out that 'eCO2R products fed to a bioproduction stage may require less purification than would be required if selling the products directly' (page 15). It is true for gas-phase products, but for the products remained in the liquid electrolyte, product separation is still necessary for the subsequent bioproduction step, particularly when a high pH electrolyte is used for eCO2R, which is incompatible with many biocatalysis processes. The authors should at least consider the issue of electrolyte.
-calculate total gas flows and electrolyte flows and use PSA and distillation reference data
R2Q1: I disagree that the costs of alkaline elctrolyzers can be used to estimate the costs of electrochemical devices used for the CO2-reduction reaction (as done in 4.2.). The materials, the peripherals etc. are very much different. (Albeit I do acknowledge that the capex has only limited impact on the results.)
-we can give examples of this being done before
R2Q2: The authors have based their energetic assessment mainly on the standard potentials (and some very few experimental values) of the respective electrochemical reactions. This is not appropriate. The formal potentials do very much differ; but even more important the overpotentials of the reactions do vary significantly for the same reaction for different electrode materials nd different current densities as well as "real" conditions. See for example here: https://www.nature.com/articles/s41578-021-00356-2, https://onlinelibrary.wiley.com/doi/abs/10.1002/adfm.202111193 Yet, it is a very dynamic field, so there will be continuous advancement This may sound too picky, but the electrochemical energetics (kinetics and overpotentials) will very much determine the cell voltage needed to derive a certain rate, yield etc. (and change the FE) and hence I do consider the here taken approach, unfortunately, as too simplified.
- This is a misinterpretation, you did not use thermodynamic potentials

## Slide 6
R4Q1: The authors do not consider high temperature options for CO2 reduction of H2 production. These routes have been shown to be more stable, higher energetic efficiency, and have higher selectivities than their low temperature alternatives. Specifically, the authors should consider CO produced in high temperature solid oxide cells at a minimum in their comparisons.
- I think it is ok to reduce the scope to low-temperature electrolysis; we can just use the adjective “low-temperature” somewhere in the intro
R4Q2: The values chosen for cell voltage, current density, and selectivity in Table S2 for a significant amount of the products are not considered state-of-the-art. Specifically, values listed for CO, Ethanol, and Acetate are not correct. Please refer to works by Wang et al. (Nature Energy 5, 478-486, 2020) for ethanol production from CO2 and Endrodi et al. (Energy & Environmental Science 13, 4098, 2020) for CO production from CO2. It is difficult to trust the results unless these values are updated, and all values should be reevaluated against current literature.
- I can put a table in the SI that cites multiple papers per chemical and maps them to the appropriate category to better justify the use of chemical tiers without choosing the specific performance from individual papers

## Slide 7
* The method for predicting full cell potential is not acceptable. A more robust value considering anode overpotential and membrane resistance should be utilized, as it is currently the full cell voltages predicted from half-cell potentials are massively underestimated leading to unreliable results. * The authors claim in lines 23-24 on page 7 that the energetic demands for hydrogen production are comparable to CO and formate. This statement is false, as hydrogen electrolyzers operate at >72% energetic efficiencies, whereas CO2 reduction processes still struggle to exceed 40% energetic efficiency. This raises questions on the comparison of the different molar H2 ratios which need to be reevaluated.